## Slide 1: Wireless Terminologies
IBM ICE (Innovation Centre for Education)
Orthogonal Frequency – division Multiplexing (OFDM) Method of encoding digital data on multiple carrier frequencies
Direct sequence spread spectrum (DSSS): Original data signal is multiplied with a pseudo random noise spreading code
Frequency hopping spread spectrum (FHSS): Method of transmitting radio signals by rapidly switching a carrier among many frequency channels
Service set identifier (SSID): A 32 alphanumeric unique identifier given to wireless local area network (WLAN)
Multiple input, multiple output-orthogonal frequency division multiplexing (MIMO-OFDM) Air interface for 4G and 5G broadband wireless communication
Temporal key integrity protocol (TKIP): A security protocol used in WPA as a replacement for WEP
Lightweight extensible authentication protocol (LEAP): It is a proprietary WLAN authentication protocol developed by Cisco
Extensible authentication Protocol (EAP) Supports multiple authentication methods, such as token cards, Kerberos, certificate etc.

## Slide 2: Wireless Networks
IBM ICE (Innovation Centre for Education)
Wireless networks use Radio Frequency (RF) signals to connect wireless – enabled devices in the network
It uses IEEE standard of 802.11 and uses radio waves for communication
Advantages
Installation is easy and eliminates wiring
Access to the network can be from anywhere within the range of an access point
Public places like airports, schools, etc. can offer constant internet connection using wireless LAN
Limitations
Wi-Fi Security may not meet the expectations
The bandwidth suffers with the number of users on the network
Wi-Fi standard changes may require replacing wireless components
Some electronics equipment can interfere with the Wi-Fi network

## Slide 3
IBM ICE (Innovation Centre for Education)
Wireless Standard
Protocol | Frequency | Bandwidth | Stream Data Rate (Mbits/s) | Modulation | Range (Meters) | 
 |  |  |  |  | Indoor | Outdoor
802.11 (Wi-Fi) | 2.4 | 22 | 1,2 | DSSS, FHSS | 20 | 100
 | 5 | 20 | 6,9,12,18,24,36,48, 54 | OFDM | 35 | 120
802.11a | 3.7 |  |  |  |  | 5000
802.11b | 2.4 | 22 | 1,2,5.5,11 | DSSS | 35 | 140
802.11d | It is an enhancement to 802.11a and 802.11b that enables global portability by allowing variation in frequencies, power levels, and bandwidth |  |  |  |  | 
802.11e | It provide guidance for prioritization of data, voice, and video transmissions enabling Qos |  |  |  |  | 
802.11g | 2.4 | 20 | 6,9,12,18,24,36, 48 54 | OFDM |  | 

## Slide 4
IBM ICE (Innovation Centre for Education)
Wireless Standard (Cont’d)
Protocol | Frequency | Bandwidth (MHz) | Stream Data Rate (Mbits/s) | Modulation | Range (Meters) | 
 |  |  |  |  | Indoor | Outdoor
802.11i | A standard for Wireless Local area Networks (MLANs) that provides improved encryption for networks that use 802.11a, 802.11b, and 802.11g standards |  |  |  |  | 
802.11n | 5 | 22 | 7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2 | MIMO- OFDM | 70 | 150
 | 2.4 | 40 | 15, 30, 45, 60, 90, 120, 135, 150 |  | 70 | 150
802.11ac | 5 | 20 | 7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2, 86.7, 96.3 | MIMO- OFDM | 35 | 
 |  | 40 | 15, 30, 45, 60, 90, 120, 135, 150, 180, 200 |  | 35 | 
 |  | 80 | 32.5, 65, 97.5, 130, 195, 260, 292.5, 325, 390, 433.3 |  | 35 | 
 |  | 160 | 65, 130, 195, 260, 390, 520, 585, 650, 780, 866.7 |  | 35 | 

## Slide 5
IBM ICE (Innovation Centre for Education)
Wireless Standard (Cont’d)
Protocol | Frequency (GHz) | Bandwidth (MHz) | Stream Data Rate (Mbits/s) | Modulation | Range (Meters | 
 |  |  |  |  | Indoor | Outdoor
802.11ad | 60 | 2160 | 6.75 Gbit/s | OFDM, single carrier, low- power single carrier | 60 | 100
802.12 | It defines demand priority, media access control protocol to increase Ethernet data rate to 100 mbps |  |  |  |  | 
802.15 | It defines communication specifications for wireless personal area networks WPANs) |  |  |  |  | 
802.15.4 | 2.5 |  | 1.3 Mbps |  | 10 | 
802.15.4 (ZigBee) | 2.4 | 868, 900 |  |  |  | 
802.15.5 | A standard for mesh networks with enhanced reliability via route redundancy |  |  |  |  | 
802.16 | A group of broadband wireless communication standards for Metropolitan Area Networks (MANs) |  |  |  |  | 

## Slide 6: Wireless Topologies
IBM ICE (Innovation Centre for Education)
Ad-hoc Standalone Network Architecture (IBSS-Independent Basic Service Set)
Devices exchange information with each other as in a peer-to-peer communication mode without the need of an access point for communication
To setup this mode up properly, first configure the wireless adapter for all the devices. They should all have the same channel name and SSID, to activate the connections
Infrastructure Network Topology (Centrally Coordinated Architecture-BSS-Basic Service Set) devices in the wireless network are connected through an access point
An access point (switch or router) connects to the internet via a modem
Installed in large organizations

## Slide 7: Typical Uses of a Wireless Networks
IBM ICE (Innovation Centre for Education)
Extensions to a Wired Network
Multiple Access Points
LAN-to-LAN wireless Network
3G Hotspot

## Slide 8
IBM ICE (Innovation Centre for Education)
Typical Uses of a Wireless Network
Access Point | It is a hardware device that allows wireless communication devices to connect to a wireless network through wireless standards such as Bluetooth, Wi-Fi- etc.
Wireless Cards (NIC) | Systems connected to the wireless network require a network interface cards (NIC) to establish a standard Ethernet connection
Wireless Modem | It is a device that receives and transmits the network signals to other units without physical cabling
Wireless Bridge | Connects multiple LANs at the MAC layer and is separated either logically or physically. It is used to increase the wireless coverage area

## Slide 9
IBM ICE (Innovation Centre for Education)
Components of a Wireless Network (Cont’d)
Wireless Repeater | Retransmits the existing signal captured from the wireless router or access point to create a new network
Wireless Router | Performs the functions of a router as well as a wireless as a wireless access point and provides internet access to various devices
Wireless Gateways | Route data packets and functions as a wireless access point. An internet connection can be shared between multiple stations
Wireless USB Adapter | Connects different devices to a wireless network in order to access the internet without a computer, router or any other network device

## Slide 10
IBM ICE (Innovation Centre for Education)
Components of a Wireless Network: Antenna
Converts electrical impulses into radio waves and vice versa | 
Directional Antenna | Omnidirectional Antenna
Used to broadcast and obtain radio wages from a single direction | It provides a 360 degree horizontal radiation pattern. It is used in wireless base stations
Parabolic Grid Antenna | Yogi Antenna
It is based on the principle of a satellite dish and can pick up Wi-Fi signals from a distance of ten miles or more | A undirectional antenna commonly used in communications for a frequency band of 10 MHz to VHF and UHF
Dipole Antenna | Reflector Antennas
Bidirectional antenna, used to support client connections rather than site-to-site applications | Reflector antennas are used to concentrate EM energy which is radiated or received at a focal point

## Slide 11
IBM ICE (Innovation Centre for Education)
WEP (Wired Equivalent Privacy) Encryption
 | WEP is a security protocol defined by the 802.11b standard; it was designed to provide a wireless LAN with a level of security and privacy comparable to a wired LAN
 | A 24-bit arbitrary number known as Initialization Vector (IV) is added to the WEP key. The WEP key and the IV together care are called as a WEP seed
 | The 64, 128, and 256-bit WEP versions use 40, 104, and 232-bit keys respectively
 | The WEP seed is used as the input for the RC4 algorithm to generate a keystream (keystream is bit-wise XORed with the combination of data and ICV to produce the encrypted data)
 | The CRC-32 checksum is used to calculate a 32-bit integrity Cehck Value (ICV) for the data, which, in turn, is added to the data frame
 | The IV field (IV+PAD+KID) is added to the cipher text to generate a MAC frame

## Slide 12
IBM ICE (Innovation Centre for Education)
WEP (Wired Equivalent Privacy) Encryption
 | WPA is a security protocol defined by 802.11i standards; it uses a Temporal Key integrity Protocol (TKIP) that utilizes the RC4 stream cipher encryption with 128- bit keys and 64-bit MIC integrity check to provide stronger encryption, and authentication
 | The temporal encryption key, transmit address, and TKIP sequence counter (TSC) is used as an input for the RC4 algorithm to generate a keystream
 | A MAC service Data Unit (MSDU) and message integrity check (MIC) are combined using the Michael algorithm
 | The combination of the MSDU and the MIC is fragmented to generate the MAC Protocol Data Unit (MPDU)
 | A 32-bit ICV is calculated for the MPDU, the combination of the MPDU and the ICV is then bitwise XORed with keystream to produce the encrypted data
 | The IV is added to the encrypted data to generate the MAC frame

## Slide 13
IBM ICE (Innovation Centre for Education)
WPA2 Encryption
WPA2 is an upgrade to WPA, it includes mandatory support for Counter Mode with Cipher Block Chaining Message Authentication Code Protocol (CCMP), an AES-based encryption mode with strong security |  | 
WPA2-Personal |  | WPA2-Enterprise
WPA2-Personal uses a set-up password (Pre-shared Key, PSK) to protect unauthorized network access |  | It includes EAP or RADIUS for centralized client authentication using multiple authentication methods, such as token cards, kerberos, certificates etc.
In PSK mode each wireless network device encrypts the network traffic using a 128-bit key that is derived from a passphrase of 8 to 63 ASCII characters |  | Users are assigned login credentials by a centralized server which they must present when connecting to the network

## Slide 14
IBM ICE (Innovation Centre for Education)
WEP vs. WPA vs. WPA2
Encryption | Attributes |  |  | 
 | Encryption Algorithm | IV Size | Encryption Key Length | Integrity Check Mechanism
WEP | RC4 | 24-bits | 40/104-bit | CRC-32
WPA | RC4, TKIP | 48-BIT | 128-BIT | Michael algorithm And CRC-32
WPA2 | AES-CCMP | 48-bit | 128-bit | CBC-MAC
WEP | Should be replaced with more secure WPA and WPA2 |  |  | 
WPA, WPA2 | Incorporates protection against forgery and replay attacks |  |  | 

## Slide 15: Wi-Fi Authentication Methods:
IBM ICE (Innovation Centre for Education)
Open System Authentication
Open System Authentication:
Any wireless device can be authenticated with the access points, allowing the device to transmit data only when its WEP key matches with the WEP key of access point

## Slide 16: Wi-Fi Authentication Methods:
IBM ICE (Innovation Centre for Education)
Shared Key Authentication
Shared Key Authentication:
The station and access point uses the same WEP key to provide authentication which means that this key should be enabled and configured manually on both the access point and the client

## Slide 17: Wi-Fi Authentication Process Using
IBM ICE (Innovation Centre for Education)
a Centralized Authentication Server
Client Access Point
RADIUS Server
1. Client requests connection
AP sends an EAP requests to determine identity
EAP response with identity Forward the identity to the RADIUS
server using the uncontrolled port
6. The wireless client responds to the RADIUS server with its credentials via the AP
8. Sends an encrypted authentication key to the AP if the credentials are acceptable
Forward the identity to the RADIUS server using the uncontrolled port
Sends a request to the wireless client via the AP specifying the
authentication mechanism to be used
7. Sends an encrypted authentication
key to the AP if the credentials are acceptable

## Slide 18
IBM ICE (Innovation Centre for Education)
Wireless Network Threats
War Driving | Rogue access Point Attack
Attackers drive around with Wi-Fi enabled laptops to detect open wireless networks | Rogue wireless access points placed in a 802.11 network can be used to hijack the connections to legitimate network users
Client Misassociation | Misconfigured Access Point Attack
An attackers sets up a rogue access point outside the corporate perimeter and tricks employees to connect to it | Misconfigured access points enable intruders to steal the SSID giving them access to the network
Unauthorized Association | Ad Hoc Connection Attack
Attackers infects a victim’s machine and activate APs provided them with an unauthorized connection to the enterprise network | Wi-Fi clients communicate directly via an ad hoc mode that does not require an AP to relay packets
HoneySpot Access Point (Evil Twin) Attack | AP MAC Spoofing
An attacker traps people by using fake hotspots | A hacker spoofs the MAC address of a WLAN client’s equipment to mask as an authorized client and connects to the AP as the client and evaesdrop the traffic

## Slide 19
IBM ICE (Innovation Centre for Education)
Wireless Network Threats (Cont’d)
Denial-of-Service Attack | WEP Cracking
Wireless DoS attacks disrupt network wireless connections by sending broadcast “de- authenticate” commands | Attackers sniff and capture packets and run a WEP cracking program to derive the WEP key
WPA-PSK Cracking | Man-in-the-Middle Attack
Attackers sniff and capture authentication packers and run a brute force attack to crack the WPA-PSK key | Attackers set up a rouge AP, and spoofs the client’s MAC address to position himself between the real AP and the client to listen to all the traffic
RADIUS Replay | Fragmentation Attack
Attackers replay the valid RADIUS server response and successfully authenticate to the to the client without valid credentials | Attackers obtain 1500 bytes of PRGA (pseudo random generation algorithm) to generate forged WEP packets which are in turn used for various injection attacks
ARP Poisoning Attack | Jamming Signal Attack
An attacker spoofs the MAC of a client and attempts to authenticate to the AP which leads to updating the MAC address info to the network routers and switches | An attacker stakes out the area from a nearby location with a high gain amplifier drowing out the legitimate access point

## Slide 20: Bluetooth Threats
IBM ICE (Innovation Centre for Education)
Leaking Calendars and Address Books
Bugging Devices
Attacker can steal user’s personal information and can use it for malicious purposes
Attacker could instruct the user’s device to make a phone call to other phones without any user interaction. They could even record the user’s conversation
Sending SMS Messages
Causing financial Losses
Terrorists could send false bomb threats to airlines using the phones of legitimate users
Hackers could send many MMS messages with an international user’s phone, resulting in a high phone bill
Remote Control
Social Engineering
Hackers can remotely control a phone to Attackers trick Bluetooth users to lower make phone calls or connect to the Internet
security or disable authentication for
Bluetooth connections in order to pair with them and steal information
Malicious Code
Protocol Vulnerabilities
Mobile phone worms can exploit a Bluetooth connection to replicate and spread itself
Attackers exploit Bluetooth pairings and communication protocols to steal data, make calls, send messages, conduct DoS attacks on a device, start phone spying, etc.

## Slide 21
IBM ICE (Innovation Centre for Education)
Wireless Network Security
Wireless Network Security Techniques | Create inventory of wireless devices
 | Placement of wireless AP and antenna
 | Disable SSID broadcasting
 | Select stronger wireless encryption mode
 | Implement MAC address filtering
 | Monitor wireless network traffic
 | Defend against WPA cracking
 | Detect rogue access points
 | Locate rogue access points
 | Protect from Denial-of-Service attacks: Interference
 | Assess wireless network security
 | Deploy Wireless IDS (WIDS) and Wireless IPS (WIPS)
 | Configure security on wireless routers